## Slide 1: PolicyBurst: Constraint-First Cloud Bursting Under Cost, Latency and Data Residency
Final Review · Project P11 · Cloud Computing
Ramanuj Agarwal · 23BCE1861
Guide: Indra Priyadarshini S. | github.com/AviatorRoyal/cloud-burst
PVT
PUB

## Slide 2: The project in one slide
A bursting controller that never breaks the budget or the residency rule, and is cheaper per unit of service when it matters
0
residency violations and ceiling breaches by PolicyBurst
227 simulated + 9 testbed runs
+80%
SLO attainment per ₹ vs threshold-only
repeated bursts, ceiling binding
2.1×
the ceiling spent by threshold-only bursting
same workload, no cost check
≈ 0 pp
attainment cost of residency at 30% restricted traffic
rises to 32 pp at 70%

## Slide 3: The problem
Threshold controllers keep pods running but ignore the rules that govern an institution's bursting decision
# typical production rule
if cpu_util > 0.75 or pending_pods > 0:
add_cheapest_public_node()
allow_any_pod_anywhere()
Operationally correct — the pods run. Administratively or legally unacceptable — the bill, the SLO and the data's jurisdiction are not checked.
Post-hoc filters are too late: the capacity is already bought when the rule rejects it.
₹
Monthly spending ceiling
Public spend is paid from an approved budget — a hard cap, not a preference.
ms
Latency objective
Distant regions add more delay than the 300 ms SLO allows.
IN
Data residency
DPDP Act 2023 §16 and sector rules (e.g. RBI 2018) keep some data in India.

## Slide 4: Objectives and how each was met
All four objectives are evidenced in code, on the testbed and in simulation
# | Objective | Evidence | Status
O1 | Controller with cost, latency and residency as explicit inputs | Feasible set per workload, then projected-spend gate (policyburst/decision.py) | Done
O2 | Implementation on private Kubernetes with a public node pool | 5-node k3s cluster, BurstPolicy CRD, tainted public pool | Done
O3 | SLO attainment per unit spend under varying burst intensity | 1.5–4× bursts, 60–300 s, testbed + simulation | Done
O4 | Capacity and cost consequences of residency | Sweep of restricted share 0–70%, with and without residency | Done
Baselines (from the problem statement): B0 no bursting · B1 threshold-only bursting without constraints.

## Slide 5: Literature gap
15 papers from 2021 onwards; none enforces all three constraints in a live private + public Kubernetes controller
Work | Hard cost ceiling | Per-destination latency | Data residency | Live private + public K8s
Starburst (ATC'24) | Partial | — | — | Full
Can't Be Late (NSDI'24) | Partial | — | — | Partial
SkyPilot (NSDI'23) | Partial | Partial | Partial | Partial
Liqo (TCC'23) | — | — | Partial | Full
Abdi et al. (FGCS'24) | Partial | — | Partial | —
Xiao et al. (FGCS'22) | Partial | — | Partial | —
K8s edge autoscalers ('21–'22) | — | — | — | Partial
PolicyBurst (this work) | Full | Full | Full | Full
“Partial” = soft objective, manual setting, or simulation only. Full gap table and references in the paper.

## Slide 6: Architecture
Standard Kubernetes primitives only: taints, cordon, node affinity, HPA — runs on any conformant cluster
Policy is a BurstPolicy custom resource; kubectl apply changes it live
Public nodes are tainted and stay cordoned until bought
Each Deployment is pinned to its permissible destinations by node affinity
HPA decides how many replicas; PolicyBurst decides where they may go

## Slide 7: Constraint-first decision, every 15 s
Residency and latency define the feasible set before the controller decides to burst
1
Observe
Pending pods, private CPU, active nodes, RTT probes
2
Residency
data class → permitted regions; unknown = restricted
3
Latency
2 × RTT + service ≤ 300 ms
4
Budget
spent + next lease ≤ ceiling − reserve
5
Act
cheapest feasible node, or reject with reason
S(t) + (Σ p(active) + p(d)) · min(lease, T − t) ≤ B − ρ # buy d only if the whole lease fits
S(t) + Σ p(active) · Δ > B − ρ ⇒ release all public # halt before the next interval crosses
release priciest node only if its pods fit on private capacity # safe scale-in (fixes thrash)
no new public node while a Deployment is mid-rollout; evict misplaced pods # rollout guard
The threshold baseline is the same loop with all three constraints switched off — so any difference comes from the decision logic, not the plumbing.

## Slide 8: Implementation
github.com/AviatorRoyal/cloud-burst · Python on the official Kubernetes client
cloud-burst/
├── policyburst/ policy · feasibility · cost
│ decision · signals · actuator · main
├── baselines/threshold.py # B1, constraints off
├── deploy/ k3s/ k3d/ crd/ policy/ app/ controller/
├── load/locustfile.py # burst + ramp shapes
├── experiments/run_matrix.py # testbed runs
├── sim/ # simulator, same code
├── analysis/ # metrics, figures
├── paper/ evidence/ results/
└── tests/ # unit tests
Commit history
270e7e3 2026-10-26 Add testbed, simulator, guards and full evaluation
b17414a 2026-10-26 Point decks at the real GitHub repo
0274ee2 2026-10-26 Initial PolicyBurst project: controller, baselines, testbed, experiments
Sample app: records (restricted) · lms (internal) · static (public); 15 ms CPU per request; HPA 60% CPU, 1–30 replicas.

## Slide 9: Testbed: a real 5-node k3s cluster
Captured on DEATHSTAR at 2026-10-25 23:55:01 UTC · evidence/20261025-235501/
$ kubectl get nodes -L p11.burst/destination,p11.burst/region
NAME STATUS ROLES AGE VERSION DESTINATION REGION
k3d-p11-agent-0 Ready <none> 3h51m v1.35.5+k3s1 private IN
k3d-p11-agent-1 Ready,SchedulingDisabled <none> 3h51m v1.35.5+k3s1 pub-in IN
k3d-p11-agent-2 Ready,SchedulingDisabled <none> 3h51m v1.35.5+k3s1 pub-sg non-IN
k3d-p11-agent-3 Ready,SchedulingDisabled <none> 3h51m v1.35.5+k3s1 pub-us non-IN
k3d-p11-server-0 Ready control-plane 3h51m v1.35.5+k3s1 private IN
$ ping -c 5 <node-ip> (avg RTT)
k3d-p11-agent-0 172.18.0.5 0.049 ms
k3d-p11-agent-1 172.18.0.3 0.051 ms
k3d-p11-agent-2 172.18.0.6 37.861 ms
k3d-p11-agent-3 172.18.0.4 119.493 ms
k3d-p11-server-0 172.18.0.2 0.060 ms
k3s v1.35.5 via k3d, 2 vCPU per node
Private: server-0, agent-0 (region IN)
pub-in IN · pub-sg +40 ms · pub-us +120 ms (netem)
Public nodes tainted, cordoned until bought
Locust load from the host, 4 processes
Same topology can be built from real VMs over Tailscale with deploy/k3s/ (planned upgrade).

## Slide 10: Evaluation method
Two layers: measure on the cluster, explore the parameter space in a simulator that runs the same decision code
1
Testbed (measured)
B0, B1, PolicyBurst · 2× burst, 180 s · 3 repetitions
Per-request logs from Locust, including the serving node
Capacity calibrated: largest load with ≥ 95% SLO attainment
2
Simulation (same Decider + CostMeter)
227 runs: 5 burst sizes × 3 durations, ablation, residency sweep
Models HPA, scheduler, pod start-up, CPU limits, closed-loop users, queues
Checked against the testbed at the shared 2× point
Metric | Definition
SLO attainment | share of all requests that succeed within 300 ms (failures count as misses)
Attainment per ₹100 | attainment points ÷ shadow-priced spend × 100
Residency violations | restricted requests served by a non-IN node (from client logs)
Residency penalty | attainment without residency − attainment with residency (pp)

## Slide 11: Testbed results (measured)
2× private capacity for 180 s, 3 repetitions per configuration, mean ± 95% CI
Config | Attainment (%) | p95 (ms) | Spend (₹) | Per ₹100 | Violations
B0 No bursting | 66.7 ± 14.5 | 1782 | 0.0 | — | 0
B1 Threshold-only | 92.8 ± 3.5 | 362 | 44.4 | 210 | 7163
PolicyBurst | 88.3 ± 14.0 | 658 | 41.0 | 229 | 0
Chart: SLO attainment per 15 s window (%), repetition 1 — burst from minute 2.0 to 5.0
| 0.0 | 0.3 | 0.5 | 0.8 | 1.0 | 1.3 | 1.5 | 1.8 | 2.0 | 2.3 | 2.5 | 2.8 | 3.0 | 3.3 | 3.5 | 3.8 | 4.0 | 4.3 | 4.5 | 4.8 | 5.0 | 5.3 | 5.5 | 5.8 | 6.0 | 6.3 | 6.5 | 6.8 | 7.0 | 7.3 | 7.5 | 7.8 | 8.0
B0 No bursting | 88.44 | 97.62 | 99.72 | 100 | 100 | 100 | 100 | 100 | 39.2 | 54.34 | 54.52 | 51.08 | 52.35 | 43.1 | 46.82 | 59.19 | 53.15 | 52.31 | 52.86 | 52.61 | 80.25 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100
B1 Threshold-only | 92.5 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 68.18 | 77.42 | 81.59 | 97.28 | 98.14 | 99.08 | 99.19 | 98.19 | 99.11 | 98.58 | 98.92 | 98.78 | 99.53 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100
PolicyBurst | 99.72 | 100 | 100 | 99.72 | 100 | 100 | 100 | 100 | 55.45 | 44.09 | 59.58 | 61.65 | 55.45 | 58.39 | 75.13 | 77.75 | 97.14 | 97.14 | 98.53 | 99.42 | 99.47 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100 | 100

## Slide 12: Does the simulation agree with the testbed?
Same configurations at the one point both cover; the simulation is then used to explore the rest
Chart: SLO attainment (%) at 2× / 180 s
| B0 No bursting | B1 Threshold | PolicyBurst
Testbed (measured) | 66.7 | 92.8 | 88.3
Simulation | 34.7 | 66.7 | 76.2
Largest gap 32 pp: 4-core testbed private pool vs 7-core model, real start-up timing
Agree: bursting beats no bursting on both platforms
PolicyBurst vs threshold: −5 pp on the testbed, +9 pp in simulation
Testbed caught what the model cannot: restricted pods leaked abroad during affinity rollouts (62 and 126 requests in early runs) — fixed with rollout + placement guards
Why: emulated pub-us is ≈120 ms RTT on the testbed (fits the SLO, so the latency filter removes nothing) but 148 ms in the model (misses it)

## Slide 13: O3: attainment per ₹ across burst sizes
PolicyBurst +41% at 1.5×, +23% at 2×, but −13% at 2.5× (simulation, 180 s bursts)
Chart: SLO attainment (%)
| 1.5× | 2× | 2.5× | 3× | 4×
B0 No bursting | 45.593 | 34.71 | 28.213 | 19.337 | 16.833
B1 Threshold-only | 75.457 | 66.69 | 54.91 | 36.003 | 30.13
PolicyBurst | 86.593 | 76.187 | 43.187 | 35.23 | 29.59
Chart: Attainment points per ₹100
| 1.5× | 2× | 2.5× | 3× | 4×
B1 Threshold-only | 232 | 205 | 174 | 110 | 92
PolicyBurst | 325 | 251 | 151 | 119 | 99
Notes: Why PolicyBurst loses at 2.5x: the static latency filter skips pub-us. At heavy overload, local queueing delay exceeds the 300 ms pub-us would add, so slow capacity would still help. Fix: a queue-aware latency filter.

## Slide 14: The ceiling holds
Five 2× bursts in one compressed billing month: threshold-only spends ₹257, PolicyBurst ₹109 (ceiling ₹120)
Chart: Cumulative spend (₹, shadow-priced)
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40
B1 Threshold-only | 0 | 0 | 0 | 0.4167 | 4.5833 | 11.5833 | 18.5833 | 25.5833 | 32.5833 | 39.5833 | 46.5833 | 53.5833 | 60.5833 | 67.5833 | 74.5833 | 81.5833 | 88.5833 | 95.5833 | 102.5833 | 109.5833 | 116.5833 | 123.5833 | 130.5833 | 137.5833 | 144.5833 | 151.5833 | 158.5833 | 165.5833 | 172.5833 | 179.5833 | 186.5833 | 193.5833 | 200.5833 | 207.5833 | 214.5833 | 221.5833 | 228.5833 | 235.5833 | 242.5833 | 249.5833 | 256.5833
PolicyBurst | 0 | 0 | 0 | 0.75 | 5.5 | 10.8333 | 16.1667 | 21.5 | 26.8333 | 32.1667 | 39.1667 | 46.1667 | 53.1667 | 60.1667 | 67.1667 | 74.1667 | 81.1667 | 88.1667 | 95.1667 | 102.1667 | 109.1667 | 109.1667 | 109.1667 | 109.1667 | 109.1667 | 109.1667 | 109.1667 | 109.1667 | 109.1667 | 109.1667 | 109.1667 | 109.1667 | 109.1667 | 109.1667 | 109.1667 | 109.1667 | 109.1667 | 109.1667 | 109.1667 | 109.1667 | 109.1667
Ceiling (₹120) | 120 | 120 | 120 | 120 | 120 | 120 | 120 | 120 | 120 | 120 | 120 | 120 | 120 | 120 | 120 | 120 | 120 | 120 | 120 | 120 | 120 | 120 | 120 | 120 | 120 | 120 | 120 | 120 | 120 | 120 | 120 | 120 | 120 | 120 | 120 | 120 | 120 | 120 | 120 | 120 | 120
Threshold-only: 2.1× the ceiling
PolicyBurst stops when the next lease would cross ceiling − reserve
Later bursts: private capacity only, rejections logged with reason “budget”
Ceiling breached: 100% of B1 runs, 0% of PolicyBurst runs

## Slide 15: Ablation: where the gain comes from
With the ceiling binding, PolicyBurst gets +80% attainment per ₹; the cost accumulator is the main source
Chart: Attainment points per ₹100 (5 bursts, 3 reps)
| B1 Threshold-only | PolicyBurst (full) | PB − cost accumulator | PB − latency filter | PB − residency filter
Attainment per ₹100 | 33.4 | 60.3 | 35.3 | 55.2 | 59.2
− cost accumulator
spend ₹251, ceiling breached every run
− latency filter
buys slow pub-us: attainment 60.1% vs 65.9%
− residency filter
57,186 restricted requests abroad per run

## Slide 16: O4: what residency costs
About zero up to 30% restricted traffic; 6 pp at 50% and 32 pp at 70%, once pub-in is saturated
Chart: Attainment penalty of residency (pp)
| 0% | 10% | 30% | 50% | 70%
Penalty (pp) | 0 | 0.1 | -5.7 | 5.9 | 31.9
Chart: Attainment of restricted requests (%)
| 10% | 30% | 50% | 70%
With residency | 80 | 81 | 64 | 39
Without residency | 80 | 76 | 75 | 75
Rule of thumb: compliance is cheap while in-country capacity (private + pub-in) can absorb the restricted share of peak demand.

## Slide 17: Hypotheses: final verdict
Reported against the hypotheses as stated, including where the data disagrees
H1
Partly supported
≥ 25% per ₹ holds at 1.5× (+41%) and with a binding ceiling (+80%); +23% at 2×; fails at 2.5× (−13%) where the static latency filter forgoes pub-us.
H2
Supported
PolicyBurst: 0 residency violations and no ceiling breach in 227 simulated and 9 testbed runs. Threshold-only served 7163 restricted requests abroad per testbed run and breached the ceiling in 100% of repeated-burst runs.
H3
Supported at 30%
Penalty at 30% restricted: -5.7 pp (bound 10 pp). Not true beyond: 5.9 pp at 50%, 31.9 pp at 70%.

## Slide 18: Threats to validity
What this setup cannot prove
!
Simulation model
Fluid queues and M/M/1-style service; checked against the testbed at one burst size.
!
One host, emulated WAN
All nodes share a machine; foreign regions are netem delay, not real links.
!
Cost is modelled
Free tier bills ₹0: shadow prices, month compressed into 1 h, rates ×100.
!
Synthetic load
Square-wave bursts; real demand ramps, overlaps and follows daily cycles.
!
Residency ≠ legal compliance
Pod placement only; logs, backups and control plane may still cross borders.
!
Small scale
5 nodes, 3 services, 3 repetitions; wide CIs at 2–2.5×.

## Slide 19: Conclusion and future work
Making constraints inputs, not filters, lets a bursting controller honour them at little cost in service
Contributions
Constraint-first bursting: feasible set per workload, projected-spend gate, safe scale-in
Open-source controller with a BurstPolicy CRD, baselines in the same code path
Evaluation on a real k3s cluster and in a simulator running the same decision code
A measured cost of residency compliance and a rule of thumb for institutions
Next
1
Queue-aware latency filter
admit a slow region when local queueing is worse — fixes 2.5×
2
Real public node
free-tier VM in an Indian region over Tailscale
3
Beyond placement
residency for logs, backups and storage

## Slide 20: Key references
[1] Luo et al., Starburst: A cost-aware scheduler for hybrid cloud, USENIX ATC 2024
[2] Yang et al., SkyPilot: An intercloud broker for sky computing, NSDI 2023
[3] Wu et al., Can't Be Late: Optimizing spot instance savings under deadlines, NSDI 2024
[4] Iorio et al., Computing without borders: The way towards liquid computing, IEEE TCC 2023
[5] Abdi, Ashjaei & Mubeen, Deadline-constrained security-aware workflow scheduling in hybrid cloud, FGCS 2024
[6] Xiao, Zhou, Yang & He, Privacy-preserving workflow scheduling in geo-distributed data centers, FGCS 2022
[7] Stoica & Shenker, From cloud computing to sky computing, HotOS 2021
[8] Wiesner et al., Let's wait awhile, Middleware 2021
[9] Ju, Singh & Toor, Proactive autoscaling for edge computing systems with Kubernetes, UCC 2021
[10] Sukprasert et al., Carbon-aware temporal and spatial workload shifting, EuroSys 2024
[11] Digital Personal Data Protection Act 2023; RBI circular on storage of payment system data, 2018
[12] Kubernetes documentation (HPA, taints, node affinity); k3s; k3d; Locust; NetEm (Hemminger 2005)

## Slide 21: Thank you — questions?
Residency, latency and budget decide where work may go — before the controller decides where it should go.